## Slide 1: Transit Traffic Engineering
Nick Feamster CS 6250: Computer Networks Fall 2011

## Slide 2: Do IP Networks Manage Themselves?
In some sense, yes:
  TCP senders send less traffic during congestion
  Routing protocols adapt to topology changes
But, does the network run efficiently?
  Congested link when idle paths exist?
  High-delay path when a low-delay path exists?
How should routing adapt to the traffic?
  Avoiding congested links in the network
  Satisfying application requirements (e.g., delay)
… essential questions of traffic engineering

## Slide 3: Outline
ARPAnet routing protocols
  Three protocols, with complexity/stability trade-offs
Tuning routing-protocol configuration
  Tuning link weights in shortest-path routing
  Tuning BGP policies on edge routers
MPLS traffic engineering
  Explicit signaling of paths with sufficient resources
  Constrained shortest-path first routing
Multipath load balancing
  Preconfigure multiple (disjoint) paths
  Dynamics adjust splitting of traffic over the path

## Slide 4: ARPAnet Routing

## Slide 5: Original ARPAnet Routing (1969)
Routing
  Shortest-path routing based on link metrics
  Distance-vector algorithm (i.e., Bellman-Ford)
Metrics
  Instantaneous queue length plus a constant
  Each node updates distance computation periodically
3
2
2
1
1
3
1
5
20
congested link

## Slide 6: Problems With the Algorithm
Instantaneous queue length
  Poor indicator of expected delay
  Fluctuates widely, even at low traffic levels
  Leading to routing oscillations
Distance-vector routing
  Transient loops during (slow) convergence
  Triggered by link weight changes, not just failures
Protocol overhead
  Frequent dissemination of link metric changes
  Leading to high overhead in larger topologies

## Slide 7: New ARPAnet Routing (1979)
Averaging of the link metric over time
  Old: Instantaneous delay fluctuates a lot
  New: Averaging reduces the fluctuations
Link-state protocol
  Old: Distance-vector path computation leads to loops
  New: Link-state protocol where each router computes shortest paths based on the complete topology
Reduce frequency of updates
  Old: Sending updates on each change is too much
  New: Send updates if change passes a threshold

## Slide 8: Performance of New Algorithm
Light load
  Delay dominated by the constant part (transmission delay and propagation delay)
Medium load
  Queuing delay is no longer negligible on all links
  Moderate traffic shifts to avoid congestion
Heavy load
  Very high metrics on congested links
  Busy links look bad to all of the routers
  All routers avoid the busy links
  Routers may send packets on longer paths

## Slide 9: Over-Reacting to Congestion
Routers make decisions based on old information
  Propagation delay in flooding link metrics
  Thresholds applied to limit number of updates
Old information leads to bad decisions
  All routers avoid the congested links
  … leading to congestion on other links
  … and the whole things repeats
I-85
GA400
ATL
Sandy Springs
“Backup at I-85” on radio triggers congestion on GA400

## Slide 10: Problem of Long Alternate Paths
Picking alternate paths
  Multi-hop paths look better than a congested link
  Long path chosen by one router consumes resource that other packets could have used
  Leads other routers to pick other alternate paths
3
2
2
1
1
3
1
5
20
congested link

## Slide 11: Revised ARPAnet Metric (1987)
Limit path length
  Bound the value of the link metric
  “This link is busy enough to go two extra hops”
Prevent over-reacting
  Shed traffic from a congested link gradually
  Starting with alternate paths that are just slightly longer
  Through weighted average in computing the metric, and limits on the change from one period to the next
New algorithm
  New way of computing the link weights
  No change to link-state routing or shortest-path algorithm

## Slide 12: Tuning Routing-Protocol Configuration

## Slide 13: Routing With “Static” Link Weights
Routers flood information to learn topology
  Determine “next hop” to reach other routers…
  Compute shortest paths based on link weights
Link weights configured by network operator
3
2
2
1
1
3
1
4
5
3

## Slide 14: Setting the Link Weights
How to set the weights
  Inversely proportional to link capacity?
  Proportional to propagation delay?
  Network-wide optimization based on traffic?
3
2
2
1
1
3
1
4
5
3
3

## Slide 15: Measure, Model, and Control
Topology/
Configuration
Offered
traffic
Changes to
the network
Operational network
Network-wide
“what if” model
measure
control

## Slide 16: Key Ingredients
Measurement
  Topology: monitoring of the routing protocols
  Traffic matrix: passive traffic measurement
Network-wide models
  Representations of topology and traffic
  “What-if” models of shortest-path routing
Network optimization
  Efficient algorithms to find good configurations
  Operational experience to identify constraints

## Slide 17: Optimization Problem
Input: graph G(R,L)
  R is the set of routers
  L is the set of unidirectional links
  cl is the capacity of link l
Input: traffic matrix
  Mi,j is traffic load from router i to j
Output: setting of the link weights
  wl is weight on unidirectional link l
  Pi,j,l is fraction of traffic from i to j traversing link l

## Slide 18: Equal-Cost Multipath (ECMP)
0.5
0.5
0.5
0.5
0.25
0.25
0.25
0.25
1.0
1.0
Values of Pi,j,l

## Slide 19: Objective Function
Computing the link utilization
  Link load: ul = Si,j Mi,j Pi,j,l
  Utilization: ul/cl
Objective functions
  min(maxl(ul/cl))
  min(Sl f(ul/cl))
f(x)
x

## Slide 20: Complexity of Optimization Problem
NP-complete optimization problem
  No efficient algorithm to find the link weights
  Even for simple objective functions
What are the implications?
  Have to resort to searching through weight settings
Clearly suboptimal, but effective in practice
  Fast computation of the link weights
  Good performance, compared to “optimal” solution

## Slide 21: Incorporating Operational Realities
Minimize number of changes to the network
  Changing just 1 or 2 link weights is often enough
Tolerate failure of network equipment
  Weights settings usually remain good after failure
  … or can be fixed by changing one or two weights
Limit dependence on measurement accuracy
  Good weights remain good, despite random noise
Limit frequency of changes to the weights
  Joint optimization for day & night traffic matrices

## Slide 22: Apply to Interdomain Routing
Limitations of intradomain traffic engineering
  Alleviating congestion on edge links
  Making use of new or upgraded edge links
  Influencing choice of end-to-end path
Extra flexibility by changing BGP policies
  Direct traffic toward/from certain edge links
  Change the set of egress links for a destination
1
2
3
4

## Slide 23: BGP Model for Traffic Engineering
Predict effects of changes to import policies
  Inputs: routing, traffic, and configuration data
  Outputs: flow of traffic through the network
Topology
BGP policy
configuration
BGP
routes
Offered
traffic
BGP routing
model
Flow of traffic through the network

## Slide 24: Reasons for Interdomain TE
Congested Edge Link
  Links between domains are common points of congestion in the Internet
Upgraded Link Capacity
  Operators frequently install higher-bandwidth links
  Aim to exploit the additional capacity
Violation of Peering Agreement

## Slide 25: Example Peering Guidelines

## Slide 26: Goals for Interdomain TE
Predictable traffic flow changes
Limiting the influence of neighboring domains
  Check for consistent advertisements
  Use BGP policies that limit the influence of neighbors
Reduce the overhead of routing changes
  Focus on small number of prefixes

## Slide 27: Tools for Interdomain TE
Essentially, adjusting local preference to affect egress point selection
Prediction
  Set of egress points per prefix
  Figure out the path from each router to egress

## Slide 28: Predictable Traffic Flow Changes
Avoid globally visible changes
  Don’t do things that would result in changes to routing decisions from a neighboring AS
  For example, make adjustments for prefixes that are only advertised via one neighbor AS

## Slide 29: Limit the Influence of Neighbors
Limit the influence of AS path length
  Consider treating paths that have “almost the same length” as a common group
Try to enforce consistent advertisements from neighbors (note: difficult problem!)

## Slide 30: Reduce the Overhead of Changes
Group related prefixes
  Don’t explore all combinations of prefixes
  Simplify configuration changes
  Routing choices: groups routes that have the same AS paths (lots of different granularities to choose from)
Focus on the (small) fraction of prefixes that carry the majority of the traffic
  E.g., top 10% of origin ASes are responsible for about 82% of outbound traffic

## Slide 31: MPLS Traffic Engineering

## Slide 32: Limitations of Shortest-Path Routing
Sub-optimal traffic engineering
  Restricted to paths expressible as link weights
Limited use of multiple paths
  Only equal-cost multi-path, with even splitting
Disruptions when changing the link weights
  Transient packet loss and delay, and out-of-order
Slow adaptation to congestion
  Network-wide re-optimization and configuration
Overhead of the management system
  Collecting measurements and performing optimization

## Slide 33: Explicit End-to-End Paths
Establish end-to-end path in advance
  Learn the topology (as in link-state routing)
  End host or router computes and signals a path
Routers supports virtual circuits
  Signaling: install entry for each circuit at each hop
  Forwarding: look up the circuit id in the table
1
2
1: 7
2: 7
link 7
1: 14
2: 8
link 14
link 8
Used in MPLS with RSVP

## Slide 34: Label Swapping
Problem: using VC ID along the whole path
  Each virtual circuit consumes a unique ID
  Starts to use up all of the ID space in the network
Label swapping
  Map the VC ID to a new value at each hop
    Table has old ID, next link, and new ID
  Allows reuse of the IDs at different links
1
2
1: 7: 20
2: 7: 53
link 7
20: 14: 78
53: 8: 42
link 14
link 8

## Slide 35: Multi-Protocol Label Switching
Multi-Protocol
  Encapsulate a data packet
    Could be IP, or some other protocol (e.g., IPX)
  Put an MPLS header in front of the packet
    Actually, can even build a stack of labels…
Label Switching
  MPLS header includes a label
  Label switching between MPLS-capable routers
IP packet
MPLS header

## Slide 36: Pushing, Popping, and Swapping
Pushing: add the initial “in” label
Swapping: map “in” label to “out” label
Popping: remove the “out” label
IP
Pushing
IP
IP
Popping
IP
Swapping
A
B
C
D
IP edge
R2
R1
R3
R4
MPLS core

## Slide 37: Constrained Shortest Path First
Run a link-state routing protocol
  Configurable link weights
  Plus other metrics like available bandwidth
Constrained shortest-path computation
  Prune unwanted links (e.g., not enough bandwidth)
  Compute shortest path on the remaining graph
Signal along the path
  Source router sends a message to pin the path to destination
  Revisit decisions periodically, in case better options exist
s
d
5, bw=10
6, bw=60
5, bw=70
3, bw=80

## Slide 38: Multipath Load Balancing

## Slide 39: Multiple Paths
Establish multiple paths in advance
  To make good use of the bandwidth
  To survive link and router failures

## Slide 40: Measure Link Congestion
Disseminate link-congestion information
  Flood throughout the network
  Piggyback on data packets
  Direct through a central controller

## Slide 41: Adjust Traffic Splitting
Source router adjusts the traffic
  Changing traffic rate or fraction on each path
  … based on the level of congestion
35%
65%

## Slide 42: Challenges
Protocol dynamics
  Stability: avoid over-reacting to congestion
  Convergence time: avoid under-reacting to congestion
  Analysis using control or optimization theory!
Protocol overhead
  State for maintaining enough (failure-disjoint) paths
  Bandwidth overhead of disseminating link metrics
  Computation overhead of recomputing traffic splits
  Implementing non-equal traffic splitting
  Hash-based splitting to prevent packet reordering
Applying the approach in an interdomain setting

## Slide 43: Conclusion: Main Issues
How are the paths expressed?
  Shortest-path routing with (changing) link weights
  End-to-end path (or paths) through the network
Timescale of routing decisions?
  Packet, flow, larger aggregates, longer timescale, …
Role of path diversity?
  Single-path routing where the one path can be changed
  Multi-path routing where splitting over paths can change
Who adapts the routes?
  Routers: through adaptive routing protocols
  Management system: through central (re)optimization