## Slide 1: White-Space Networking
Nick Feamster CS 6250
Fall 2011
(slides from Rohan Murty)

## Slide 2: Motivation
Bandwidth becoming scarcer and more valuable
  Increased demands on wireless applications
  Users demand higher performance
Dynamically accessing multiple channels can increase spectrum efficiency
Our goal is to support multiple transmissions and increase performance by mitigating interference

## Slide 3
Higher Frequency
Wi-Fi (ISM)
Broadcast TV

## Slide 4: What are White Spaces?
dbm
Frequency
-60
-100
“White spaces”
470 MHz
700 MHz
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
are Unoccupied TV Channels
White Spaces
54-90
170-216
Wireless Mic
TV Stations in America
  50 TV Channels
  Each channel is 6 MHz wide
FCC Regulations*
    Sense TV stations and Mics
    Portable devices on channels 21 - 51

## Slide 5: The Promise of White Spaces
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
54-90
174-216
Wireless Mic
More Spectrum
Longer Range
Up to 3x of 802.11g
at least 3 - 4x of Wi-Fi

## Slide 6: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
1
2
3
4
5
Each TV Channel is 6 MHz wide
 Use multiple channels for more bandwidth
Spectrum is Fragmented
Chart: # Contiguous Channels
| 1 | 2 | 3 | 4 | 5 | 6 | >6
Urban | 0.739 | 0.231 | 0 | 0.028 | 0 | 0 | 0
Suburban | 0.716 | 0.15 | 0.056 | 0.056 | 0 | 0.018 | 0
Rural | 0.367 | 0.122 | 0.122 | 0.102 | 0.081 | 0.04 | 0.14

## Slide 7: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
Location impacts spectrum availability
 Spectrum exhibits spatial variation
Cannot assume same
channel free everywhere
1
2
3
4
5
Spatial Variation
TV
Tower

## Slide 8: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
Incumbents appear/disappear over time
 Must reconfigure after disconnection
Spatial Variation
Cannot assume same
channel free everywhere
1
2
3
4
5
1
2
3
4
5
Temporal Variation
Same Channel will
not always be free
Any connection can be
disrupted any time

## Slide 9: Channel Assignment in Wi-Fi
Fixed Width Channels
 Optimize which channel to use
1
6
11
1
6
11

## Slide 10: Spectrum Assignment in WhiteFi
1
2
3
4
5
Spatial Variation
 BS must use channel iff free at client
Fragmentation
 Optimize for both, center channel and width
1
2
3
4
5
Spectrum Assignment Problem
Goal
Maximize Throughput
Include
Spectrum at clients
Assign
Center Channel
Width
&

## Slide 11: Accounting for Spatial Variation
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

=
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

1
2
3
4
5

## Slide 12: Intuition
BS
Use widest possible channel
Intuition
1
3
4
5
2
Limited by most busy channel
But
Carrier Sense Across All Channels
All channels must be free
  ρBS(2 and 3 are free) = ρBS(2 is free) x ρBS(3 is free)
Tradeoff between wider channel widths
and opportunity to transmit on each channel

## Slide 13: Discovering a Base Station
Can we optimize this discovery time?
1
2
3
4
5
Discovery Time = (B x W)
1
2
3
4
5
How does the new client discover channels used by the BS?
BS and Clients must use same channels
Fragmentation
 Try different center channel and widths

## Slide 14: SIFT, by example
ADC
SIFT
Time
Amplitude
10 MHz
5 MHz
SIFT
Pattern match in time domain
Does not decode packets
Data
ACK
SIFS